Far Horizons Arduino Library for TI CC1101

###### V 0.1 September 23, 2013
Started by Lou Nigra
###### Process
1. Start with a copy of RADIO library folder provided by Bharat Uddagiri:

   RADIO LIBRARY FOR TI RADIO MODUELS
   RADIO_CC110L.h - CC110L module library
  Author : BHARAT UDDAGIRI
  Version : 0.1
  DATE : MARCH 9, 2012
  EMAIL : UDDAGIRI@GMAIL.COM
    This library is designed to use CC110L module on Arduino platform.

2. Rename the folder and the .h and .cpp files with a descriptive name consistent with standard naming conventiones:

Folder RadioCC1101FH -> RadioCC1101FH.h and RadioCC1101FH.cpp

Edit the above information at the beginning of the files accordingly and make sure to make reference to the original author’s file.

3. Create new functions listed below to make controlling code for the CC1101 simpler. Use as examples the existing declarations, prototypes and functions (class methods, actually) in RADIO.h, RADIO.cpp and if necessary, consult a tuturial on creating Arduino libraries:

http://arduino.cc/en/Hacking/LibraryTutorial

Mapping desired sensible values to the required bit values of the various byte registers bit is difficult. Use as an example the frequency setting method found in:

projects/TwoWayComm/scratchpad/MonitorRSSI/MonitorRSSI.ino

Required Class Methods:

void setBaseFrequency( int freqMhz )
int getRSSI( int channell ) (NOTE: Returns the raw reading, not converted to dbm)
void setChannel( int channel )
void setChannelWidth( int chanWidthKHz )
void setBaudRate( float rateKHz )