//Timer interrupt Test trial
//Jeididah Oyeyemi
//june 29 2013
#include <SPI.h>
#include <RADIO.h>

int sensorValue = 0; // variable to store the value coming from the sensor
int mode;//
int Speed=5000;
void RegConfigPrint();
//innitializing all buffers
byte RegBuffer[50]={0};
byte TX_Buffer[10]={0};
byte RX_Buffer[10]={0};
byte i,length;
void setup (void)
{
mode=0;

Serial.begin (9600);
//Serial.flush();
//Serial.print("set up");
setSPI();
setInterrupt1();
}
void loop(void){
// Serial.flush();
while (mode !=7){

 Serial.println("frame start");
unsigned long start=millis();
delay(2000);
unsigned int count = millis()-start;
Serial.print(count);
 Serial.println("frame end");
}}

void setSPI(void)
{
   SPI.begin ();
   SPI.setClockDivider(SPI_CLOCK_DIV4);
   SPI.setBitOrder(MSBFIRST);
   SPI.setDataMode(SPI_MODE0) ;

}

ISR(TIMER1_COMPA_vect)//first timer interrupt
{//Serial.flush();
  //Serial.println("work?");
if(mode==0)//transmit mode
{ Speed=7000;
  //long start=millis();
 // long count=0;
  setTX();//switching to transmit mode
  TX_Buffer[1]=TX_Buffer[1]+1;
  TX_Buffer[2]=TX_Buffer[2]+2;
  TX_Buffer[3]=3;
  TX_Buffer[4]=4;
  TX_Buffer[5]=5;
  TX_Buffer[6]=6+TX_Buffer[1];
  CC110L.SendData(TX_Buffer,61);
  Serial.println("mode0");
 // count=millis()-start;// calculating the time that haspassed by
  Speed=7812;//-count*7812/500;
  mode=1;

}
else{//recieve mode
//
Serial.println("mode1");
setRX();//switching to reieve mode
//unsigned long start=millis();
int rec=0;
int count=0;
while (count<10000)
{ //Serial.println("stuck?");

   if(CC110L.CheckReceiveFlag())
 {
   int size=CC110L.ReceiveData(RX_Buffer);
 //Serial.println(size);
  rec=1;
  break;
 }
//count=millis()-start;
count++;
}
if(rec==1){
 for(i=0;i<10;i++)
   {
      Serial.print(RX_Buffer[i],DEC);
// Serial.print(' ',BYTE);
    }
  }

mode=0;
//count=millis()-start;// calculating the time that haspassed by
Speed=7812;//-count*7812/500;//the recieve portion has 500ms so im taking the alloted time nd subtracting the time that passed buy
}
//Serial.println("reset");

//Serial.println(mode);
//Serial.println("after");
setInterrupt1();//resetting the next interrupt
}

void setInterrupt1(void)//sets up the conditions of interrupt1
 { noInterrupts(); // disable all interrupts
   // initialize timer1
// Serial.print("set");

 //setting up SPI

 //set timer1 interrupt at 1Hz
  TCCR1A = 0;// set entire TCCR1A register to 0
  TCCR1B = 0;// same for TCCR1B
  TCNT1 = 0;//initialize counter value to 0
  // set compare match register for 1hz increments

  OCR1A = Speed;// = (16*10^6) / (1*1024) - 1 (must be <65536)
  // turn on CTC mode
  TCCR1B |= (1 << WGM12);
  // Set CS10 and CS12 bits for 1024 prescaler
  TCCR1B |= (1 << CS12) | (1 << CS10);
  // enable timer compare interrupt
  TIMSK1 |= (1 << OCIE1A);

  interrupts(); // enable all interrupts

      }
void setTX(void)
{

  CC110L.GDO_Set();
  CC110L.Reset();
  CC110L.RegConfig();
  CC110L.PATABLE();

// SpiWriteReg(0x09,0x10);
//CC110L.WriteSingleReg(0x09,0x09);
//CC110L.WriteSingleReg(0x06,0xC9);
CC110L.ReadBurstReg(0,RegBuffer,47);
for( i=0;i<61;i++)
  {
     TX_Buffer[i]=0;
  }

}
void setRX(void)
{

  CC110L.GDO_Set();
  CC110L.Reset();
  CC110L.RegConfig();
  //CC110L.PATABLE();
  CC110L.SetReceive();
}
void RegConfigPrint()
{
  for(int i = 0; i<=50;i++)
{

  Serial.print ("REG ADD :");
  Serial.print (i,HEX);
  Serial.print (" ");
  Serial.print("Value : ");
  Serial.print (RegBuffer[i],HEX);
  Serial.println(" ");

  delay (1000); // 1 second delay

}
}